## Slide 1
“Prediction of building energy consumption”
Energy AI Track Kim Sohee
Amasyali, Kadir, and Nora M. El-Gohary. "A review of data-driven building energy consumption prediction studies."
Renewable and Sustainable Energy Reviews 81 (2018): 1192-1205.
Notes: A review on the prediction of building energy consumption
https://doi.org/10.1016/j.rser.2012.02.049
Zhao, Hai-xiang, and Frédéric Magoulès. "A review on the prediction of building energy consumption."
Renewable and Sustainable Energy Reviews 16.6 (2012): 3586-3592.
A review of data-driven building energy consumption prediction studies
https://doi.org/10.1016/j.rser.2017.04.095

## Slide 2
Prediction models
Rely on thermodynamic rules for detailed energy modelling and analysis
Software : EnergyPlus, eQuest, and Ecotect
  Calculate building energy consumption based on detailed building and environmental parameters
Detailed data may not be available to the users at the time of simulation
  Failure to provide accurate input can result in poor prediction performance
-1-
Engineering models (Physical models)
> eQuest
(Building energy analysis program)
> EnergyPlus
(whole building energy simulation program)
> EcoTect
Notes: There are several popular methods used for forecasting building energy consumption, that can be categorized into two main approaches, engineering and data-driven approach.
First, Engineering models rely on thermodynamic rules for detailed energy modelling and analysis.
Examples of building energy simulation software that utilize physical models include EnergyPlus, eQuest, and Ecotect.
These types of software calculate building energy consumption based on detailed building and environmental parameters such as building construction details; operation schedules; HVAC design information; and climate, sky, and solar/shading information.
The pictures shows each software program.
EneryPlus is a whole building energy simulation program, and eQuest is a building energy analysis program.
Ecotect is a program that supports architect's design through analysis of various factors of building performance for energy efficiency and sustainable design.
However, some of such detailed data may not be available to the users at the time of simulation.
Failure to provide accurate input can result in poor prediction performance.

## Slide 3
Learns from historical/available data for prediction
Correlate the energy consumption or energy index with the influencing variables
4 steps : data collection, data preprocessing, model training, and model testing
Machine learning algorithms : SVM, ANN, decision trees, and other statistical algorithms
-2-
Prediction models
Data-driven models
Notes: Data-driven modelling does not perform such energy analysis or require such detailed data about the simulated building, and instead learns from historical/available data for prediction. They correlate the energy consumption or energy index with the influencing variables.
Data-driven prediction has gained a lot of research attention in recent years, despite its possible limitations.
Developing a data-driven model, typically, consists of four primary steps: data collection, data preprocessing, model training, and model testing.
SVM, ANN, decision trees, and other statistical algorithms are the most commonly-used supervised machine learning algorithms for model training.
This table summarizes the features used in the reviewed models.

## Slide 4
-5-
Data-driven models Limitations
  Data-driven prediction models may not perform well outside of their training range.
  Black-box models – their internals are not known
    Hybrid or grey-box modelling approaches (physical + data-driven)
Prediction models
[77] Chae YT, Horesh R, Hwang Y, Lee YM. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings. Energy Build2016;111:184–94.
[98] Dong B, Li Z, Rahman SMM, Vega R. A hybrid model approach for forecasting future residential electricity consumption. Energy Build 2016;117:341–51.
Notes: Despite the importance of data-driven approaches, It has two main limitations.
First, Data-driven prediction models may not perform well outside of their training range.
And they are black-box models, their internals are not known.
On the other hand, Hybrid or grey-box modelling approaches offer a combination of physical and data-driven prediction models, thereby leveraging the advantages and minimizing the disadvantages of both approaches.
There are several papers which developed a hybrid model.
Tae Chae et al. utilized ANN to forecast sub-hourly electricity usage in a commercial building complex [47]. It was seen that the ANN with15-min interval data forecasted accurately with more training data. The Mean Bias Error by taking 1, 2, 3 and 4 weeks for training are −10.4,−5.6, −2.3 and 0.03 respectively.
Chae et al. [48] developed forecasting models using ANN for sub-hourly electricity usage for a commercial building complex. The input variables that were selected for model development were the day type, time of day, HVAC set-point temperature schedules, outdoor air dry-bulb temperature and humidity. The results show that the daily peak prediction with past four weeks’ training data performs the best. Three training methods that were used were Static, accumulative and sliding window with average APE of 3% and 4.5% for weekdays of August and September

## Slide 5
-5-
Prediction models
[77] Chae YT, Horesh R, Hwang Y, Lee YM. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings. Energy Build2016;111:184–94. http://dx.doi.org/10.1016/j.enbuild.2015.11.04
[98] Dong B, Li Z, Rahman SMM, Vega R. A hybrid model approach for forecasting future residential electricity consumption. Energy Build 2016;117:341–51. http:// dx.doi.org/10.1016/j.enbuild.2015.09.033