## Slide 1
“Prediction of building energy consumption”
Energy AI Track Kim Sohee
A hybrid model approach for forecasting future residential electricity consumption. Energy Build 2016;117:341–51.
Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings. Energy Build2016;111:184–94.
Notes: A review on the prediction of building energy consumption
https://doi.org/10.1016/j.rser.2012.02.049
Zhao, Hai-xiang, and Frédéric Magoulès. "A review on the prediction of building energy consumption."
Renewable and Sustainable Energy Reviews 16.6 (2012): 3586-3592.
A review of data-driven building energy consumption prediction studies
https://doi.org/10.1016/j.rser.2017.04.095

## Slide 2
Contents
Prediction models for forecasting building energy consumption
Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
A hybrid model approach for forecasting future residential electricity consumption

## Slide 3
Rely on thermodynamic rules for detailed energy modelling and analysis
Software : EnergyPlus, eQuest, and Ecotect
  Calculate building energy consumption based on detailed building and environmental parameters
Detailed data may not be available to the users at the time of simulation
  Failure to provide accurate input can result in poor prediction performance
Engineering models (Physical models)
> eQuest
(Building energy analysis program)
> EnergyPlus
(whole building energy simulation program)
> EcoTect
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models for forecasting building energy consumption
Prediction models
Notes: There are several popular methods used for forecasting building energy consumption, that can be categorized into two main approaches, engineering and data-driven approach.
First, Engineering models rely on thermodynamic rules for detailed energy modelling and analysis.
Examples of building energy simulation software that utilize physical models include EnergyPlus, eQuest, and Ecotect.
These types of software calculate building energy consumption based on detailed building and environmental parameters such as building construction details; operation schedules; HVAC design information; and climate, sky, and solar/shading information.
The pictures shows each software program.
EneryPlus is a whole building energy simulation program, and eQuest is a building energy analysis program.
Ecotect is a program that supports architect's design through analysis of various factors of building performance for energy efficiency and sustainable design.
However, some of such detailed data may not be available to the users at the time of simulation.
Failure to provide accurate input can result in poor prediction performance.

## Slide 4
Learns from historical/available data for prediction
Correlate the energy consumption or energy index with the influencing variables
4 steps : data collection, data preprocessing, model training, and model testing
Machine learning algorithms : SVM, ANN, decision trees, and other statistical algorithms
Data-driven models
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models for forecasting building energy consumption
Prediction models
Notes: Data-driven modelling does not perform such energy analysis or require such detailed data about the simulated building, and instead learns from historical/available data for prediction. They correlate the energy consumption or energy index with the influencing variables.
Data-driven prediction has gained a lot of research attention in recent years, despite its possible limitations.
Developing a data-driven model, typically, consists of four primary steps: data collection, data preprocessing, model training, and model testing.
SVM, ANN, decision trees, and other statistical algorithms are the most commonly-used supervised machine learning algorithms for model training.
This table summarizes the features used in the reviewed models.

## Slide 5
Data-driven models Limitations
  Data-driven prediction models may not perform well outside of their training range.
  Black-box models – their internals are not known
    Hybrid or grey-box modelling approaches (physical + data-driven)
Black-box model
  Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings.
  Chae YT, Horesh R, Hwang Y, Lee YM. Energy Build 2016;111:184–94.
Grey-box model (hybrid)
  A hybrid model approach for forecasting future residential electricity consumption.
  Dong B, Li Z, Rahman SMM, Vega R. Energy Build 2016;117:341–51.
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models for forecasting building energy consumption
Prediction models
Data-driven models
Physical models
Prediction
models
Notes: Despite the importance of data-driven approaches, It has two main limitations.
First, Data-driven prediction models may not perform well outside of their training range.
And they are black-box models, their internals are not known.
On the other hand, Hybrid or grey-box modelling approaches offer a combination of physical and data-driven prediction models, thereby leveraging the advantages and minimizing the disadvantages of both approaches.
There are several papers which developed a hybrid model.
Tae Chae et al. utilized ANN to forecast sub-hourly electricity usage in a commercial building complex [47]. It was seen that the ANN with15-min interval data forecasted accurately with more training data. The Mean Bias Error by taking 1, 2, 3 and 4 weeks for training are −10.4,−5.6, −2.3 and 0.03 respectively.
Chae et al. [48] developed forecasting models using ANN for sub-hourly electricity usage for a commercial building complex. The input variables that were selected for model development were the day type, time of day, HVAC set-point temperature schedules, outdoor air dry-bulb temperature and humidity. The results show that the daily peak prediction with past four weeks’ training data performs the best. Three training methods that were used were Static, accumulative and sliding window with average APE of 3% and 4.5% for weekdays of August and September

## Slide 6: 2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings.
Chae YT, Horesh R, Hwang Y, Lee YM.
Energy Build 2016;111:184–94.
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models

## Slide 7
Forecasting electricity load – commercial & industrial buildings
  To be able to better manage energy usage
The short-term load forecast (STLF) – a period shorter than a day → more interest
  ∵ The utility prices may change by seasonality, time-of-use in on/off peak period, and contract demand
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Introduction
7/30
Notes: Forecasting electricity load, especially for commercial and industrial buildings has become one of the more important topics recently, to be able to better manage energy usage.
Although the forecast time horizon can range from minutes to years, the short-term load forecast (STLF), especially for a period shorter than a day, has been more of an interest in the perspective of buildings / because the utility prices may change by seasonality, time-of-use in on/off peak period, and contract demand.

## Slide 8: 2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Escriva-Escriva et al. – STLF model using ANNs
  Requires an entire whole year’s data set
  Not be stable when the energy consumption pattern has large daily or annual variability
The short-term load forecast (STLF) – sub-hourly electricity consumption of buildings
A short-term load forecasting model using data mining and machine learning technique while assuming limited availability of data.
ANN models – commercial building complex
Introduction
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Notes: Previous studies on STLF for the sub-hourly electricity consumption of buildings are limited.
Escriva-Escriva et al. [14] proposed STLF model using ANNs,
but this model requires an entire whole year’s dataset / and the performance may not be stable when the energy consumption pattern has large daily or annual variability.
Therefore, it is useful to explore a model that can perform well under more general setting, in particular, not requiring a large amount of input data for forecasting electricity usage of buildings.
For this need, they developed a short-term load forecasting model using data mining and machine learning technique while assuming limited availability of data.
In particular, they investigate ANNs model to predict the energy consumption of a commercial building complex.

## Slide 9
Three office buildings in urban area
  15,224
  All managed by one utility billing system
Description of a case study: a building complex
5 floor
4 floor
2 floor
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Methodological approach
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Notes: The site consists of three office buildings in urban area, each of which has different number of floors.

## Slide 10
Data collection and processing
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Methodological approach
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Notes: The relational database management system (RDBMS) has been used to collect and store environmental variables, BMS data, and electricity usage as illustrated here.
Dataset has over 1000 data points with 20 different measurement types. / some variables are not used for forecast.
So the predictors are divided into 3 categories ->

## Slide 11
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Methodological approach
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Data collection and processing
Environmental data
  ODT, ODH, PPT, RAN, WSD, SKC
Time indicator
  DTF, TIF
Operational condition
  OPC
> Potential predictor variables
9 potential variables
Notes: Environmental data, time indicator, and operational condition.
The data include outdoor air temperature, relative humidity, wind speed and direction, sky condition, and precipitation(강수량) type in every 3-hour interval for the next 72 hours. The forecast data is updated eight times a day.
And RDBMS converts string variables into numeric variables as shown.
An averaged system operation schedule of five CAV systems was used as the HVAC operational condition.
However, In nine independent variables, some variables can decrease model accuracy, stability, and effectiveness. Therefore, it is necessary to pre-screen the variables by identifying the important variables from the input data set.

## Slide 12
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Methodological approach
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Feature extraction for dimension reduction
Random forests algorithm
+ Previous electricity usages
5 variables
Notes: So Random forests algorithm was used to assess the importance of variables by measuring the candidate parameters in terms of their impacts on the response of prediction.
The permutation importance and Node impurity were used to select variables in this study
The permutation importance estimates the importance of each predictor by considering prediction error variation when the variable is permuted but others are kept the same. Node impurity is measured by the total decrease in residual sum of squares from splitting on the variable, averaged over all trees.
Variables are ranked by both relative importance metrics in left figure.
According to this, Outdoor air temperature, relative humidity and operational condition has more importance.
It has a similarity to the conditional permutation importance at right Table.
So, these 5 variables are ranked highly in their importance.
These and previous electricity usages are selected as input variables.

## Slide 13
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Methodological approach
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Predictive model selection
> 9 machine-learning algorithms
ANN model architecture
15-min interval data set (energy consumption)
5 predictor variables (July 1st ~ July 31st, 2012)
  Train : 2880 data points for 6 input variables
Notes: Next, In this study, they examined nine different machine-learning algorithms and chose the one that performed best, the ANN.
The 15 minute interval data set of Ei / and highly ranked 5 predictor variables were collected from July 1st to July 31st, 2012. Total of 2880 data points for 6 input variables including electric usage were used to train the model.

## Slide 14
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Results and discussion
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Network design parameters - Hidden layer architecture and time-delayed inputs
Training
Evaluation

## Slide 15
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Results and discussion
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Model implementation
> Comparisons of actual observed and forecasted electricity usage

## Slide 16
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Results and discussion
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Model implementation

## Slide 17
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Results and discussion
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Model implementation
> Actual forecast result

## Slide 18: 3. A hybrid model approach for forecasting future residential electricity consumption
Dong B, Li Z, Rahman SMM, Vega R. Energy Build 2016;117:341–51..
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models

## Slide 19
Data-driven - Black-box : machine learning driven, derived by measured data
  Limited in one type of methods (neural networks)
Physical + Data-driven = Grey-box
  Built upon physical relationship – parameters of physical model are unknown or uncertain.
  + Measured data → identify those parameters, model tuning for better accuracy
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Introduction
Commercial vs Residential building
The lack of hourly or more granular data
The growing percentage of miscellaneous electrical load (MEL) in residential building (~52%)
A new hybrid modeling approach
Forecast hour ahead and 24 ahead residential electrical load
기타 전기부하 비율
Notes: “Data-Driven” models rely more on the data, assuming there is already a mathematical relationship between inputs (e.g. weather parameters) and outputs (e.g. total building energy consumptions).
To further categorize the “Data-Driven” approach, there are “black-box” and “grey-box” models.
The “black-box” model is purely machine learning driven and derived by measured data. Previous studies on energy consumption forecasting using “black-box” models are limited in one type of methods such as neural networks.
The “Grey-box” model is built upon physical relationships, while the parameters of the physical model are usually unknown or uncertain.
The measured data is used to identify those parameters and model tuning for better accuracy.
The “Grey-box” models have been applied widely to estimate commercial building heating and cooling load, not many on the residential building sector.
The research gap between commercial and residential building comes from two main sources,
which are (a) the lack of hourly or more granular data 세분화된 데이터, and (b) the growing percentage of miscellaneous electrical load (MEL) 기타 전기 부하 비율의 증가 in residential building, respectively.
It is 15-25% but expected to increase 52% by 2040.
But for residential building, none of Previous models can work as good as, because MEL is not weather related, and occupies a large portion of total building energy consumption.
So in this paper they try to close this gap by developing a new hybrid modeling approach through integrating “physical” and “data-driven” models
to forecast hour ahead and 24 h ahead residential electrical load.

## Slide 20
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Current state of the art
Data-driven models – machine learning algorithms
  ANN, SVR, LS-SVM, GPR, GMM
  Only conducted on total building energy consumption forecast
Physical models (Forward models) - Use laws of thermodynamics (열역학)
  2 main parts : Building thermal zone envelopes / Air conditioning modeling
  Physical phenomena (convection, conduction, radiation) → 1 layer
  All layers (walls, floor, roof, etc.) → Thermal envelope zone (thermal resistance-capacity (RC) networks)
  Suffers from a lack of building information
  Limited to thermal usage prediction such as air conditioning
A new hybrid modeling approach
Forecast both total and air-conditioning (AC) energy consumption
Notes: Physical models use laws of thermodynamics. There are two main parts of a model:
building thermal zone envelopes and air conditioning modeling.
For simplicity, most models integrate all physical phenomena (convection, conduction, and radiation) to one layer, and all layers (walls, floor, roof, etc.) to a thermal envelope zone. Thus, the envelope of the thermal zone in a building can be constructed as thermal resistance-capacity (RC) networks.
In energy forecast applications, physical model suffers from a lack of building information
Furthermore, many tests involved in data-driven methods are only conducted on total building energy consumption forecast.
In contrast, physical models are limited to thermal usage prediction such as air conditioning.
Our research proposes a hybrid approach, making use of forward and data-driven models to forecast both total and air-conditioning (AC) energy consumptions.

## Slide 21
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Methodology and approach
Test bed and performance metrics
4 residential houses in San Antonio (110 each)
  SIP (Structure Insulated Panel)
  ACC (Autoclaved Aerated Concrete)
  Container
  Stick
Material information
Calibrated thermal resistances and capacities – manufactures (119mm SIP U-value is 0.22)
Energy consumption – 5 min intervals for all rooms
Outdoor air temperature, global horizontal solar radiation – weather station near the position
Solar radiations on the surface – sensors installed on site
Hour ahead, 24-h ahead models – evaluated
% of error per prediction
Smaller is better
Variation of overall prediction
Smaller, more similar dispersions
Notes: The residential data in our research was collected from four residential houses in San Antonio as shown. Those four samples are single family dwelling around 110 m2 each.
Houses are named according to construction materials: SIP, ACC, Container, and Stick.
For material information, // those are measured by each places. /// calibrated thermal resistances and capacities are provided by manufacturers. Energy consumptions are monitored at 5 min intervals for all the rooms including kitchen, bathroom, living and bedroom areas. Sub-metered data such as plugs, lighting, water heater and AC are also available. Outdoor air temperature and global horizontal solar radiation are collected from a weather station near the position. Solar radiations on the surface of each house at the same period are measured from sensors installed on site. ///
Hour ahead and 24-h ahead models are evaluated using performance metrics: mean absolute percentage error (MAPE), and coefficient of variation (CV) of root mean square error.

## Slide 22
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Methodology and approach
Hybrid model
Historical information → Forecast non-AC electricity consumption → Internal heat gain
Predicted weather + internal gain forecast → The thermal network differential algebraic equations (DAEs) → Zone temperature + Set point schedule → AC regression model
AC + non-AC = a total electricity consumption
Notes: First, we forecast non-AC electricity consumption from historical non-AC consumption information. As internal heat gain is highly correlated with non-AC electricity consumption, it can be directly estimated from the non-AC prediction using heat convection and conduction.
Secondly, predicted weather together with the internal heat gain forecast are inputted to the thermal network differential algebraic equations (DAEs)to simulate zone temperature. Then, the calculated zone temperature change is updated to an AC regression model with a set point schedule. Afterward, the AC cooling power consumption is further predicted. By summing up the AC and non-AC predictions, we have a total electricity consumption.

## Slide 23
24-hour ahead
  Previous 24-31 h historical load + moving averages
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Methodology and approach
Hybrid model
Non-AC forecast
AC forecast
Hour ahead
  Previous 1-5 h historical load information
P : electricity consumption forecast
: minutes resolution AC cooling or heating load in the forecast time window
COP : coefficient of performance
m : time scale (if q = 5min temporal load, m=1/12)
Notes: For the non-AC forecast, the target is the non-AC energy consumption standing for plug load, lighting, water heater etc.
The hour ahead input set, defined as H1, is used to forecast the non-AC load L_t at hour.
The features are this, where Lt−1 represents the historical non-AC electricity consumption for the previous 1 h.
For the hour ahead forecast case, input shows that the features need previous 1–5 h historical load information.
The 24-h ahead input set, defined as H2, is used to forecast the next 24-h load Lt to Lt+23
For one future time load Lt of the next 24-h window, the required input features are these.
They needs not only previous 24–31 h historical load but also moving averages.
For the AC forecast, electricity consumption of the AC system can be found, as expressed by this equation.

## Slide 24
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Results and discussions
Air-conditioning
Train - 1 week ~ 1 month before tested period (before 2013.9.17)
Test - 1 week (2013.9.17 ~ 2013.9.24)
AC / non-AC / total building energy consumption
# MAPE
SIP : 7.03%
ACC : 8.29%
Container : 9.15%
Stick : 8.03%
> SIP house
Insensitivity
Transitional stages
Peak
> MAPE
Notes: For evaluation of the hybrid approach, 1 week from 2013.9.17 to 2013.9.24 is tested for all the residential houses. One week up to 1 month of non-AC power consumption data before the tested period is used for training.
The experimental results of forecasting are organized in the following order: AC, non-AC, and total building energy consumption.
As the first step of hybrid modeling approach, we need to forecast the AC air conditioning energy usage.
MAPEs are like this for each houses. An example of SIP house is plotted as this.
Most errors are beyond the baseline are due to the insensitivity of the model to AC cooling peak or transitional stages.
With an R squared value of 0.9629 shown in next figure, the forecasts show fairly accurate predictions on AC power consumption.

## Slide 25
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Results and discussions
Non-air-conditioning
> Sinusoid shape
> Irregular shape
Hour
24 h
Forecasting performance↓
Insensitive
Over fitting
Forecasting performance↓
Notes: Next, For the non-AC energy forecasting, they conducted a comparative analysis of five data-driven methods (ANN, SVR, LSSSVM, GPM and GMM). These are results of SIP and ACC houses.
They present 2 types of common energy patterns observes : Sinusoid사이너소이드 and irregular shaped.
For the sinusoid patterns, traditional methods have good performances with MAPE below 10%.
For the irregular patterns, some methods are still able to account for the larger variation, but forecasting performance decreased.
Results of 24-h ahead forecasts are significantly different than hour ahead cases.
They cannot keep the same performance for 24-hour ahead cases.
The predictions are either over fitting or insensitive as shown.

## Slide 26
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Results and discussions
Non-air-conditioning
> 1 month of SIP
Inability to capture the random spikes
→ Short period of time (5 min)
Reduced performance due to
Constraints on input feature
  Hour : previous 1~5 h
  24-h : yesterday
  → Key assumption :
    Daily usages are similar without large deviation
Random behavior of residents creates the randomness
Notes: The reduced performance for 24-h ahead forecasts is due to model limitations and input constraints.
Constraints on input feature selections are not obvious in hour ahead cases since the training features include previous 1-5 hour.
However, for 24-hour ahead, models learned the patterns only from yesterday.
Thus, the successfully prediction of longer forecast window is based on one key assumption: daily usages are similar without large deviation, 매일 사용량이 유사하다.
This figure shows an example for forecasting a longer period, 1 month, using representative techniques, SVR, ANN and GPR.
Most large forecast error reveal models’ inability to capture the random spikes in energy consumption
that occur for short period of time, like within 5 minute.

## Slide 27
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Results and discussions
Total energy consumption

## Slide 28
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Results and discussions
Total energy consumption

## Slide 29
2. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
3. A hybrid model approach for forecasting future residential electricity consumption
1. Prediction models
Results and discussions
Discussions