## Slide 1
“Prediction of building energy consumption”
Energy AI Track Kim Sohee
A hybrid model approach for forecasting future residential electricity consumption. Energy Build 2016;117:341–51.
Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings. Energy Build2016;111:184–94.
Notes: A review on the prediction of building energy consumption
https://doi.org/10.1016/j.rser.2012.02.049
Zhao, Hai-xiang, and Frédéric Magoulès. "A review on the prediction of building energy consumption."
Renewable and Sustainable Energy Reviews 16.6 (2012): 3586-3592.
A review of data-driven building energy consumption prediction studies
https://doi.org/10.1016/j.rser.2017.04.095

## Slide 2
Prediction models
Rely on thermodynamic rules for detailed energy modelling and analysis
Software : EnergyPlus, eQuest, and Ecotect
  Calculate building energy consumption based on detailed building and environmental parameters
Detailed data may not be available to the users at the time of simulation
  Failure to provide accurate input can result in poor prediction performance
-1-
Engineering models (Physical models)
> eQuest
(Building energy analysis program)
> EnergyPlus
(whole building energy simulation program)
> EcoTect
1/30
Amasyali, Kadir, and Nora M. El-Gohary. "A review of data-driven building energy consumption prediction studies."
Renewable and Sustainable Energy Reviews 81 (2018): 1192-1205.
Notes: There are several popular methods used for forecasting building energy consumption, that can be categorized into two main approaches, engineering and data-driven approach.
First, Engineering models rely on thermodynamic rules for detailed energy modelling and analysis.
Examples of building energy simulation software that utilize physical models include EnergyPlus, eQuest, and Ecotect.
These types of software calculate building energy consumption based on detailed building and environmental parameters such as building construction details; operation schedules; HVAC design information; and climate, sky, and solar/shading information.
The pictures shows each software program.
EneryPlus is a whole building energy simulation program, and eQuest is a building energy analysis program.
Ecotect is a program that supports architect's design through analysis of various factors of building performance for energy efficiency and sustainable design.
However, some of such detailed data may not be available to the users at the time of simulation.
Failure to provide accurate input can result in poor prediction performance.

## Slide 3
Learns from historical/available data for prediction
Correlate the energy consumption or energy index with the influencing variables
4 steps : data collection, data preprocessing, model training, and model testing
Machine learning algorithms : SVM, ANN, decision trees, and other statistical algorithms
-2-
Data-driven models
Prediction models
Notes: Data-driven modelling does not perform such energy analysis or require such detailed data about the simulated building, and instead learns from historical/available data for prediction. They correlate the energy consumption or energy index with the influencing variables.
Data-driven prediction has gained a lot of research attention in recent years, despite its possible limitations.
Developing a data-driven model, typically, consists of four primary steps: data collection, data preprocessing, model training, and model testing.
SVM, ANN, decision trees, and other statistical algorithms are the most commonly-used supervised machine learning algorithms for model training.
This table summarizes the features used in the reviewed models.

## Slide 4
-5-
Data-driven models Limitations
  Data-driven prediction models may not perform well outside of their training range.
  Black-box models – their internals are not known
    Hybrid or grey-box modelling approaches (physical + data-driven)
[77] Chae YT, Horesh R, Hwang Y, Lee YM. Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings. Energy Build2016;111:184–94.
[98] Dong B, Li Z, Rahman SMM, Vega R. A hybrid model approach for forecasting future residential electricity consumption. Energy Build 2016;117:341–51.
Prediction models
Notes: Despite the importance of data-driven approaches, It has two main limitations.
First, Data-driven prediction models may not perform well outside of their training range.
And they are black-box models, their internals are not known.
On the other hand, Hybrid or grey-box modelling approaches offer a combination of physical and data-driven prediction models, thereby leveraging the advantages and minimizing the disadvantages of both approaches.
There are several papers which developed a hybrid model.
Tae Chae et al. utilized ANN to forecast sub-hourly electricity usage in a commercial building complex [47]. It was seen that the ANN with15-min interval data forecasted accurately with more training data. The Mean Bias Error by taking 1, 2, 3 and 4 weeks for training are −10.4,−5.6, −2.3 and 0.03 respectively.
Chae et al. [48] developed forecasting models using ANN for sub-hourly electricity usage for a commercial building complex. The input variables that were selected for model development were the day type, time of day, HVAC set-point temperature schedules, outdoor air dry-bulb temperature and humidity. The results show that the daily peak prediction with past four weeks’ training data performs the best. Three training methods that were used were Static, accumulative and sliding window with average APE of 3% and 4.5% for weekdays of August and September

## Slide 5: Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings.
Chae YT, Horesh R, Hwang Y, Lee YM.
Energy Build 2016;111:184–94.

## Slide 6: Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Introduction
Forecasting electricity load – commercial & industrial buildings
  To be able to better manage energy usage
The short-term load forecast (STLF) – a period shorter than a day → more interest
  ∵ The utility prices may change by seasonality, time-of-use in on/off peak period, and contract demand
Notes: Forecasting electricity load, especially for commercial and industrial buildings has become one of the more important topics recently, to be able to better manage energy usage.
Although the forecast time horizon can range from minutes to years, the short-term load forecast (STLF), especially for a period shorter than a day, has been more of an interest in the perspective of buildings / because the utility prices may change by seasonality, time-of-use in on/off peak period, and contract demand.

## Slide 7: Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Introduction
Escriva-Escriva et al. – STLF model using ANNs
  Requires an entire whole year’s data set
  Not be stable when the energy consumption pattern has large daily or annual variability
The short-term load forecast (STLF) – sub-hourly electricity consumption of buildings
A short-term load forecasting model using data mining and machine learning technique while assuming limited availability of data.
ANN models – commercial building complex
Notes: Previous studies on STLF for the sub-hourly electricity consumption of buildings are limited.
Escriva-Escriva et al. [14] proposed STLF model using ANNs,
but this model requires an entire whole year’s dataset / and the performance may not be stable when the energy consumption pattern has large daily or annual variability.
Therefore, it is useful to explore a model that can perform well under more general setting, in particular, not requiring a large amount of input data for forecasting electricity usage of buildings.
For this need, they developed a short-term load forecasting model using data mining and machine learning technique while assuming limited availability of data.
In particular, they investigate ANNs model to predict the energy consumption of a commercial building complex.

## Slide 8: Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Methodological approach
Three office buildings in urban area
  15,224
  All managed by one utility billing system
Description of a case study: a building complex
5 floor
4 floor
2 floor
Notes: The site consists of three office buildings in urban area, each of which has different number of floors.

## Slide 9: Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Methodological approach
Data collection and processing

## Slide 10: Artificial neural network model for forecasting sub-hourly electricity usage in Commercial buildings
Methodological approach
Data collection and processing